## Slide 1
Link Analysis
StaticListAutomationManagement
LinkList
Each link: none/one/multiple automations
File-based
Updates written back to file
fileName: fileProfileInstance
Automation Management
Visualization of Automation Management
Link group related automation
TimeBasedPowerSaving
Switch power saving on/off depending on trigger occurence
Monitored parameter: time
When trigger a is met prepare the list of links:
  read the list of links from StaticList filtered for an assigned TimeBasedPowerSaving automation, exclude all links from the BlackListManagement
Multiple triggers (StringProfiles) of types:
  StartPowerSaving
  RestoreFullCapacity
Times when to change between operation modes configurable (StringProfile)
Link group related switching operation
SimpleActivation
PersistentDeactivation
[list of links]
Cyclic operation to iterate over input list of links, activates RedundantTransmittersOff
Sequential
No retries
RedundantTransmittersOff
AllTransmittersOn
Cyclic operation to iterate over input list of links, activates AllTransmittersOn
Sequential
No retries, maximum runtime (profile)
Link related switching operation
[activate sequentially for each link in list]
Activate power saving mode on a link after ensuring both transmitters of a parallel link are operating at their maximum configured modulation
Find required link information via BasisLinkAnalysis
1 rollback attempt; status reporting
BasicLinkAnalysis
[link-ID]
[list of links]
Translates passed link-ID into uuid of related AirLayer connection
Analyzes if there is a parallel AirLayerConnection
Determines mount names, uuids, local-Ids of ther Air Interface that terminate
  the AirLayer connection
  and parallel AirLayer connection
Reads transmitterIsOn, transmissionModeMax, transmissionModeCur
Returns all data in responseBody; if data incomplete returns error instead
[found info]
Power saving status
Centrally documented & made available information about:
For which links power saving mode is currently activated
Individual links/link-list filtered by status
BasicPowerSavingStatus
Logging of power saving
No module yet, in backlog for v1.0.0
Would be good to log at least
when a power switching was triggered
And if it was successful or not
Data rentention can be configurable by IntegerProfile (days)
Performance of power savings
Alarm management of power savings
BlackListManagement
for BlackList links power saving MUST not be configured
ElasticSearch
[activate sequentially for each link in list]
Module overview
(AIPS v1.0.0)
Others: e.g. utilization
MWGW
StaticList: Removal of links or unassignments require to check if power savings need to be switched off  call allTransmittersOn for all (previously) assigned automations
BlackList: add link
turn-off its power saving (if active)
doesn‘t change assignments in staticList, but link is skipped during later processing until removed from BlackList
Prep list of links
Start/Stop services for TBPS are not started auomatically (with embed-yourself), but only on demand!
When input link list for SimpleActivation/PersistentDeactivation is determined, links on BlackList are skipped
SimpleActivation/PersistentDeactivation have own link queues. If power saving trigger is met, the link is added to the related queue together with the related automationName. A link can be there with multiple entries (same or different automationName); links are added at the end of the queue.
purge services: just stop executing SA/PD actions for not yet processed links in queue (by emptying queue); no rollbacks performed here.
E.g. in case TBPS end trigger is met: first stop all outstanding actions from SA (call SA-purge-queue), then call service to PD services to deactive the power saving.
Switching transmitter on/off requires writing to devices
Done via MicroWaveDeviceGateway
A link L1 connects AirInterfaces (A1-B1) on 2 devices (A,B). It can have a parallel link L2, which also connectes A & B, but from different AirInterfaces (e.g. A2-B3).
BasicLinkAnalysis has a service to resolve the AirInterface address info (2 triplets) for a link:
  Input: linkID; Output: 2 triples (mount-name, uuid (airInterface), local-id (ltp)); 1 triple for each side of the link.
  It is called for L1; to find the parallel link L2, BLA needs to search on the same device A for other AirInterfaces that also have a connection to an AirInterface on device B. (Different AirfInterfaces than for L1).
If the parallel link is found, transmissionMode information can be retrieved for it (via its AirInterface address info).
BLA only returns the data, but does not perform checks on it.
Find connection information not part of MWDI, but MWNI (MWDI will evolve to MWNI)
But: MWDI will be extended already provide these required services for AIPS
is link in power saving mode?
Deactivates power saving mode for a link by switching on all transmitters of the link
(reads power saving status of the link from BasicPowerSavingStatus first to see if it needs to do anything)
1 rollback attempt; status reporting
[found info]
LinkId | AutomationNames
101550001 | DayBasedPowerSaving
205550004 | TimeBasedPowerSaving;UtilizationBasedPowerSaving
206552300 | 
… | 
StaticList
LinkId
101550001
601550002
…
BlackList
LinkId | deviationsFromOriginalState | modulesToRestoreOriginalState
101550001 | RedundantTransmittersOff; TransmitterPowerAdaption | AllTransmittersOn; RestoreTransmitterPower
205550004 | RedundantTransmittersOff | AllTransmittersOn
206552300 | <empty, no powerSaving active> | <empty>
601550002 |  | 
PowerSavingStatus table
Status must indicate, a) which module has activated powerSavingStatus (i.e. why there is a deviation from the original state (= no powerSaving active)): deviantsFromOriginalState and b) how to bring the link back into original state (modulesToRestoreOriginalState)
3rd-party applications can use this information to restore the original state
Original state (power-saving=off): both module lists are empty
sync with staticList periodically to remove dead records
Link related switching operations first call PowerSavingStatus for the given link to determine, if they even have to do something; if not they immediately return a „success“
RedundantTransmittersOff: asks PowerSavingStatus, if deviationsFromOriginalState has an entry for RedundantTransmittersOff; if yes: done
AllTransmittersOn: asks PowerSavingStatus if modulesToRestoreOriginalState does NOT contain AllTransmittersOn; if not, then done.
Note: might lead to issues if powerSavingStatus records could not be set properly due to DCN issues (might require some manual work to fix the status)
Link related automation
DroppedFramesInitiatedRestoration
Monitor the droppedFramesOutput counter
Retrieval interval & threshold are configured via profileInstances (modification via OAM layer); initial values could be interval=5min and threshold=1
If the monitoring detects that droppedFramesOutput for a link > threshold, it initiates restoring the original powerSaving mode, i.e. turning of power saving.
Note: droppedFramesOutput is not supported by all vendors/devices.
If a link A should be turned off and ist parallel link B is already turned off, B‘s transmitter is off and its current transmissionMode is also missing; so nothing is done for A
droppedFrameOutput cannot be checked for RedundantTransmittersOff!
linkId needs to be translated into AirInterface address data and then the related EthernetContainers needs to be identified for the found airInterface address information.
For this limited approach 7 requests per link are necessary, for some data from previous executions may be reused (address info not likely to change)
MWDI
Note: counters/attributes need to be checked on both sides of the (parallel) link
MWDI

## Slide 2
Link analysis
StaticListAutomationManagement
addLinksToStaticList(linkIdList)
assignAutomationToLinks(automationName,linkIdList)
--------------------
removeLinksFromStaticList(linkIdList)
unassignAutomationFromLinks(automationName,linkIdList)
unassignAllAutomationsFromLinks(linkIdList)
unassignAutomationFromAllLinks(automationName)
-------------------
listLinks(optional: linkIdList)
listAutomationNames()
listAssignmentsForSpecificLink(linkId)
listLinksWithSpecificNumberOfAssignments(number)
listLinksWithSpecificAutomationAssigned(automationName)
Automation Management
Visualization of Automation Management
Link group related automation
TimeBasedPowerSaving
addStartTrigger(time)
addEndTrigger(time)
removeStartTrigger(time)
removeEndTrigger(time)
removeAllTriggers()
------------------
listAllTriggers()
------------------
startTimeBasedPowerSaving()
stopTimeBasedPowerSaving()
Link group related switching operation
SimpleActivation
PersistentDeactivation
addLinksToPowerSavingActivationQueue(linkIdList, automationName, switchingOperationName)
removeLinksFromPowerSavingActivationQueue(linkId, switchingAutomationName)
purgePowerSavingActivationQueue()
RedundantTransmittersOff
AllTransmittersOn
addLinksToPowerSavingDeactivationQueue(linkIdList, automationName, switchingOperationName)
purgePowerSavingDeactivationQueue()
Link related switching operation
switchRedundantTransmitterPairOff(linkId, automationName)
BasicLinkAnalysis
resolveAirInterfaceAddressTriples(linkId)
analyzeStatusOfParallelLink(linkId)
Power saving status
recordPowerSavingStatus(linkId, addDeviationsFromOriginalState, removeDeviationsFromOriginalState, addModulesToRestoreOriginalState, removeModulesToRestoreOriginalState)
---------------------
listPowerSavingStatus()
listPowerSavingStatusOfLink(linkId)
listAffectedLinks(deviationFromOriginalState)
listToBeRestoredLinks(moduleToRestoreOriginalState)
-------------
syncPowerSavingStatusListWithStaticLinkList()
BasicPowerSavingStatus
Logging of power saving
module in backlog for v1.0.0
Performance of power savings
Alarm management of power savings
BlackListManagement
MWDI
ElasticSearch
addLinksToBlackList(linkIdList)
----------------
removeLinksFromBlackList(linkIdList)
---------------
listLinksInBlackList()
isLinkBarred(linkId)
Offered Services
(AIPS v1.0.0)
active power savings to be deactivated
Check if active power savings need to be deactivated
MWGW
Ggf.: add diagram names
reactivateTransmittersOfLink(linkId, automationName)
Link related automation
DroppedFramesInitiatedRestoration
startMonitoring()
stopMonitoring()
MWDI

## Slide 3
removeLinksFromStaticList(linkIdList)
listLinks(linkIdList)
Remove linkIdList from file
Async deactivation: for each linkId from linkIdList:
  Extract the list of assigned automationNames for the linkId from (1)-data
  For each found automationName: deactivate power saving with parameters (linkId, automationName):
    stop possibly ongoing SimpleActivations via removeLinksFromPowerSavingActivationQueue(linkId, automationName)
    Initiate PersistentDeactivation: addLinksToPowerSavingDeactivationQueue(linkId, automationName)
unassignAutomationFromLinks(automationName,linkIdList)
listLinks(linkIdList)
Remove automationName for all linkIds from linkIdList
Async deactivation: for each linkId from linkIdList:
  Check if automationName is found in (1)-data; if not skip link
  else:
    stop possibly ongoing SimpleActivations via removeLinksFromPowerSavingActivationQueue(linkId, automationName)
    Initiate PersistentDeactivation: addLinksToPowerSavingDeactivationQueue(linkId, automationName)
unassignAllAutomationsFromLinks(linkIdList)
unassignAutomationFromAllLinks(automationName)
listLinks(linkIdList)
listLinksInBlackList()
Add links from linkIdList to the BlackList
Async deactivation: for each linkId from linkIdList:
  Skip linkId if found in list from (2)
  Else: find automationNames for the linkId in data from (1)
  For each found automationName: deactivate power saving with parameters (linkId, automationName):
    stop possibly ongoing SimpleActivations via removeLinksFromPowerSavingActivationQueue(linkId, automationName)
    Initiate PersistentDeactivation: addLinksToPowerSavingDeactivationQueue(linkId, automationName)
addLinksToBlackList(linkIdList)
listLinksWithSpecificAutomationAssigned(automationName)
Remove automationName for all found linkIds from (1)
Async deactivation: for each linkId from linkIdList returned by (1):
    stop possibly ongoing SimpleActivations via removeLinksFromPowerSavingActivationQueue(linkId, automationName)
    Initiate PersistentDeactivation: addLinksToPowerSavingDeactivationQueue(linkId, automationName
Concept for asynchronous power saving deactivation